## Slide 1
DIGITAL DESIGN PROJECT
4-bit ALU
RTL Design • Functional Verification • Logic Synthesis • Formal Equivalence Checking
Xcelium (irun)
SimVision
IMC
Genus
Conformal LEC
Prepared by Pratheep D
Cadence EDA Flow

## Slide 2
PROJECT OVERVIEW
What the ALU Does, and How It Was Proven Correct
1
RTL Design SystemVerilog ALU with 3-bit opcode selecting 8 operations
2
Functional Verification Self-checking testbench simulated in Xcelium (irun)
3
Coverage Sign-off Block, expression and toggle coverage measured in IMC
4
Logic Synthesis Mapped to a 90nm standard-cell library using Genus
5
Formal Verification RTL vs. netlist equivalence proven with Conformal LEC
SUPPORTED OPERATIONS
ADD
opcode 000
SUB
opcode 001
AND
opcode 010
OR
opcode 011
XOR
opcode 100
NOT
opcode 101
SHL
opcode 110
SHR
opcode 111
02

## Slide 3
RTL DESIGN
ALU Block Architecture
alu_4bit
combinational
always_comb + case(opcode)
a [3:0]
b [3:0]
opcode [2:0]
result [3:0]
carry_out
zero
DESIGN NOTES
Language: SystemVerilog Style: fully combinational Overflow: carry_out on ADD/SUB/shift Flag: zero asserted when result = 0
File: alu_4bit.sv
03

## Slide 4
VERIFICATION METHODOLOGY
From RTL to Signed-off Coverage
1
Testbench
13 self-checking
vectors, task-based
2
Simulate
Xcelium (irun)
-access +rwc -gui
3
Waveform
SimVision
signal inspection
4
Coverage
IMC block / expr /
toggle metrics
Result: all 13 test vectors PASSED • 0 mismatches (errors = 0)
04

## Slide 5
SIMULATION RESULTS
Xcelium Console Output
13 / 13
VECTORS PASSED
0
ERRORS
130 ns
SIM RUNTIME
ALL TESTS PASSED
05

## Slide 6
WAVEFORM ANALYSIS
SimVision Signal Trace
WHAT'S SHOWN
a[3:0], b[3:0] operands sweep across all 8 opcodes
result[3:0] bit-level breakdown alongside carry_out
errors = 0 confirms no mismatch at any timestep
zero flag stays low — no zero-result vector in this window
06

## Slide 7
FUNCTIONAL COVERAGE
IMC Coverage Sign-off
Metric | Score
Overall | 87.3%
Block | 95.24%
Toggle | 100%
Expression | 33.33%
Toggle coverage at 100% shows every signal bit switched both directions; the lone gap is Expression coverage, expected for a case-based combinational block whose default branch is never driven.
07

## Slide 8
LOGIC SYNTHESIS
Genus RTL-to-Gate Flow
read_libs
90nm lib
read_hdl
alu_4bit.sv
elaborate
syn_generic
syn_map
syn_opt
54
STANDARD CELLS
68
INTERNAL NETS
17
I/O PORTS
Netlist written to alu_4bit_netlist.v — target: 90nm standard-cell library (slow.lib)
08

## Slide 9
GATE-LEVEL NETLIST
Synthesized Schematic (Genus)
54
LEAF CELLS
17
TERMS
68
NETS
09

## Slide 10
PPA SUMMARY
Area, Power & Timing Reports
AREA
291.41
µm² total cell area
54 cells
POWER
9.91
µW total power
leak 11% • int 57% • sw 32%
TIMING
+6434
ps worst slack
constraint MET
POWER BREAKDOWN
Chart: 
| Leakage | Internal | Switching
Power | 11.35 | 56.59 | 32.06
Critical path: opcode[0] → result logic → zero, 1566 ps data-path delay against a 10 ns virtual-clock budget — comfortable positive slack.
10

## Slide 11
FORMAL VERIFICATION
Conformal Logic Equivalence Checking
6 / 6
OUTPUT POINTS EQUIVALENT
Golden: alu_4bit.sv (RTL) — 8 library cells, 14 primitives Revised: alu_4bit_netlist.v — 54 synthesized cells Compared outputs: result[3:0], carry_out, zero
Formal LEC checks equivalence exhaustively across all input combinations — a stronger guarantee than simulation coverage alone.
11

## Slide 12
SUMMARY
Front-End Flow: Complete
RTL designed in SystemVerilog — 8 ALU operations, carry & zero flags
Functionally verified in Xcelium — 13 / 13 test vectors passed
Coverage signed off in IMC — 100% toggle, 95%+ block coverage
Synthesized in Genus — 54-cell netlist, timing constraint met (+6434 ps slack)
Formally verified in Conformal — RTL ≡ netlist across all 6 outputs
Next: physical design (place & route) in Innovus
Tools: Cadence Xcelium • SimVision • IMC • Genus • Conformal
12